## Slide 1: Lab 2

## Slide 2: MIPS Variables
Type of variable:
word (4 Bytes)
half (2 Bytes)
byte (1 Byte)

## Slide 3: Load and Store Instructions
Load : Memory -> Register
Store: Register -> Memory

## Slide 4: Load
lw
  copy word (4 bytes) at source memory address to destination register
  lw can be replaced with lb or lh depending on the type of variable that is being loaded
    lb or lbu if variable is of type byte (1 Byte)
    lh or lhu if variable is of type half (or half word = 2 Bytes)
a: .word 0
lw t0, a

## Slide 6: Load address
la t0, var1
  Copy memory address of var1 (a variable defined in the program) into register t0
Indirect Addressing
  lw t2, (t0)
    load word at memory address contained in t0 into t2
  sw t2, (t0)
    store word in register t2 into memory at address contained in t0

## Slide 7: Exercise
If memory address of variable x is 0x10010001,
la t0, x
lw t1, 16(t0)
lw t1, -12(t0)
t1 stores the value at which memory address?

## Slide 8: Load Immediate
li register_destination, value
  Loads immediate value in destination register

## Slide 9: Store Instructions

## Slide 10: Lab Overview